## Slide 1: CMSIS-DAP: Overview + Enhancements (v1.2.0)
Firmware implemented on Cortex-M MCU
Cortex-M4
CMSIS-DAP
CoreSight
Cortex-M23
CoreSight
Cortex-A7
CoreSight
Debug Unit
JTAG/ SWD
Device
May be integrated on a single evaluation board
USB
inputs
Debugger
Host PC
    CMSIS-DAP v1.2.0
    Adds “real-world” timer to the Debug Unit
    Introduces trace recording for custom Performance Counters (inputs), for example:
    Power measurement (U, I) from A/D converters
  Performance parameters from a external system (i.e. wait states)
  Transfer parameters of an RF interface
SWO
    Many platforms supported

## Slide 2: CMSIS-DAP v1.2.0 trace data management
Debug Unit
A/D input
    Trace sources are recorded in blocks
      Block size 512 bytes … 2 Kbytes
      Includes Time Stamp and Channel No.
    Trace communication optionally with data difference compression
    SWO trace is handled in same way
      Improves SWO trace performance
SWO
CMSIS-DAP
counter
Trace Source
Time Stamp | Channel No. | Trace Data
Time Stamp | A/D #2 | Trace Data
Time Stamp | SWO | Trace Data
Time Stamp | A/D #1 | Trace Data
Time Stamp | SWO | Trace Data
Time Stamp | SWO | Trace Data
Time Stamp | free | ---
Time Stamp | free | ---

## Slide 3
Firmware implemented on Cortex-M MCU
Cortex-M
CMSIS-DAP
CoreSight
Cortex-M
CoreSight
Cortex-A
CoreSight
Debug Unit
JTAG/ SWD
Device
May be integrated on a single evaluation board
USB
Debugger
Host PC
SWO
UART

## Slide 4
Debug Unit
Arm Cortex-M based microcontroller
TCK/SWCLK
TMS/SWDIO
TDI
TDO/SWO
nTRST
nRESET
UART RX
UART TX
JTAG/SWD
USB
Status LEDs
Debugger connected
Target running

## Slide 5
Debug Unit
Arm Cortex-M based microcontroller
TCK/SWCLK
TMS/SWDIO
TDI
TDO/SWO
nTRST
SWDIO Out-Enable
nRESET
UART RX
UART TX
JTAG/SWD
USB
Status LEDs
Debugger connected
Target running
Isolation
TCK/SWCLK
TMS/SWDIO
TDI
TDO/SWO
nTRST